## Slide 1: CS M51A Discussion #2
Hyunjin Kim

## Slide 2: Outline
Lecture Review
  2-out-of-5 code
Homework#1 Review
Chapter 2
  Example 2.18
  One-set and Zero-set
  Minterm and Maxterm
  Conversion Simplified SOP ↔ POS

## Slide 3: Ex2.18: A lock control
Input: CLASS ∈ {0, 1, 2, 3}
GROUP ∈ { A, B, C }
Output: LOCK ∈ { OPEN, CLOSED}
Function: LOCK
OPEN if CLASS≥2 and GROUP = A
CLOSE otherwise
->get a switching expression of Lock.

## Slide 5
L=C1’C0’G1G0 + C1’C0G1G0
= C1’G1G0(C0’ + C0)
= C1’G1G0 -> simplified one by BA
Not, C1’G0 due to don’t care -> K-map

## Slide 9: SOP ↔ POS
Single product term or Single sum term
  SOP is same as POS vice-versa
  Since there are interpreted in both ways.
Example
 | The term can be interperted either way. | 
 | SOP | POS
a | Single product | Single sum
ab | Single product | two sums
abc | Single product | three sums
abcd | Single product | four sums
a+b | two products | Single sum
a+b+c | three products | Single sum
b+c+d | three products | Single sum
a+b+c+d | four products | Single sum

## Slide 10: SOP ↔ POS
Use distributive property more than single term
  SOP -> POS
    A+(BC) = (A+B)(A+C)
  POS -> SOP
    A(B+C) = AB + AC
Simplified SOP and its corresponding simplified POS
If don’t care exists, the conversion does not always work.
SOP | POS
ab + c | (a+c)(b+c)
ab+c+d =(a+c)(b+c)+d =(a+c+d)(b+c+d) | (a+c+d)(b+c+d)
ab+bc | (a+c)b
ab+bc+d =b(a+c)+d =(b+d)(d+(a+c)) =(b+d)(a+c+d) | (b+d)(a+c+d)