## Slide 1: CSM51A Discussion Week #1
Hyunjin Kim

## Slide 2: Outline
Number conversion
  binary, Octal, Hexadecimal, or Decimal
  fixed or mixed-radix
Signed Integer Representation
Boolean Algebra (Appendix A)

## Slide 3: Integer Domain Conversion
Decimal: 10i
Binary: 2i
Example
  37
  511
  (10111101)2
  (1234)8
  (EC76)16 ->(?)8
Decimal | Binary
0 | 0000
1 | 0001
2 | 0010
3 | 0011
4 | 0100
5 | 0101
6 | 0110
7 | 0111
8 | 1000
9 | 1001
10 | 1010
11 | 1011
12 | 1100
13 | 1101
14 | 1110
15 | 1111

## Slide 5: Mixed-Radix
X=(x, y, z) is a 3-digit weighted mixed-radix number system: x is a radix-16, y is a radix-3, and z is a radix-12
  Convert X=(6, 1, 11) to a decimal number
  The largest number of X in decimal?
LargetstX = rn-1 x rn-2 x … x r0 -1 = 16 x 3 x 12 - 1 = 576 – 1 = 575

## Slide 6: Why 2’s complement
Sign-and-Magnitude
  Two zero
  Signs of result depends on sign of number with the larger magnitude (additional operation)
1’s complement
  Two zero
  End around carry (additional operation)

## Slide 7: SM add/sub

## Slide 8: 1’s Complement add/sub

## Slide 9: 2’s complement
Simpler Addition scheme makes two’s complement the most common integer number systems in digital systems.

## Slide 14: Overflow Detection in Addition
Overflow
  Result exceeds most positive or negative representable integer
    -2n-1 ≤ z ≤ 2n-1-1
  Both operands same sign, result opposite sign
    overflow = x’n-1y’n-1zn-1 + xn-1yn-1z’ n-1
      X is positive and Y is positive but the sum Z is negative
      X is negative and Y is negative but the sum Z is positive

## Slide 15: Overflow Detection
ov = cn XOR cn-1

## Slide 16: +/- in 2’s complement