## Slide 1: CS 33 Discussion
Week 8

## Slide 2: Cache Coherence

## Slide 3: Cache Coherence
Assume:
Multiple cores, each with private L1$
Shared L2$
What if multiple L1$ have same blocks?
Reads only: No problem.
Writes: How to notify other cores?

## Slide 4: Cache Coherence
Snooping Coherence Protocol
Write-Through L1$
Cores listen (snoop) on shared bus
If another core writes to a block:
  Write-Invalidate: Remove own copy
  Write-Update: Update own copy
Core1 L1$
L2$
Shared Bus
Core0 L1$

## Slide 5: Cache Coherence
Snooping Coherence Protocol
Write-Invalidate
Just need to set Valid=0.
Write-Update
Need to write entire cache block.
Requires another cache port.
More expensive in latency, area, power, etc.

## Slide 6: Cache Coherence
MSI Directory Protocol
Each block can be in state M, S, or I.
M: Modified
  Block is present in L2$
  Zero or one L1$ has block, with write permission
S: Shared
  Block is present in L2$
  Zero or more L1$ also have a read-only copy
I: Invalid
  Block is not present in L2$ or any L1$

## Slide 7: Memory Consistency